## Slide 1: Rudimentary Rockets
Lauren Koch

## Slide 2
Variations on the Runge-Kutta method are applied for each stage
Rocket parameters: rocket mass, fuel mass, burn rate, velocity of fuel ejection, drag coefficient, reference area
Planet parameters: mass, radius, molar mass of atmosphere, average temperature, surface pressure
Calculates the flight path of a simple model rocket launched from a planet

## Slide 3: Stage 1
Stage 2
Stage 3
Proceeds until fuel is exhausted
dvdt = (Fth – Fg – Fd)/M(t)
Compared against the Tsiolkovsky rocket equation
Proceeds until maximum vertical height is achieved
Proceeds until the rocket returns to the ground
dvdt = (-Fg – Fd)/M
dvdt = (-Fg + Fd)/M

## Slide 4
Rocket parameters
  10,000 kg rocket
  10,000 kg fuel
  100 kg/s burn rate
  7000 m/s fuel ejection velocity
  0.5 drag coefficient
  10 m2 reference area
Planet parameters (Earth)
  0.0286 molar mass of atmospheric gas
  282.32 K average temperature
  101,325 Pascal surface pressure